FINAL Cruise Instructions

ECO-FOCI

NOAA Ship MILLER FREEMAN, Cruise MF-07-08

May 19 – May 28, 2007

Chief Scientist – Annette Dougherty, NOAA/AFSC

- DRAFT CRUISE INSTRUCTIONS

  - Cruise Title – Ecosystem and Fisheries-Oceanography Coordinated Investigations (Eco-FOCI).

  - Cruise Numbers:

    - Cruise Number – MF-07-08.

    - Eco-FOCI Number – 5MF07.

  - Cruise Dates:

    - Departure - Depart Saturday, May 19, 2007, at 1500 hours from Dutch Harbor, Alaska.

    - Arrival – Arrive Monday, May 28, 2007 at 0800 hours in Kodiak, Alaska.

  - Operating Area – Unimak Pass to Shelikof Strait and northeast Kodiak Island, with the survey ending survey at Kodiak Island, Alaska.

- CRUISE OVERVIEW

  - Cruise Objectives - The objectives of this cruise are to conduct an ichthyoplankton survey and process oriented studies in the region between Unimak Pass, the Shumagin Islands, and through Shelikof Strait to Kodiak Island, Alaska, so that we may estimate the abundance, transport, and factors influencing the survival of young walleye pollock larvae.  We will also occupy stations on Line 8 to continue our 22-year time series of environmental and biological conditions in Shelikof Strait.

  - Applicability - These instructions, with FOCI Standard Operating Instructions for NOAA Ship MILLER FREEMAN, dated March 29, 2007, present complete information for this cruise.

  - Participating Organizations

NOAA - Pacific Marine Environmental Laboratory (PMEL)

7600 Sand Point Way N.E., Seattle, Washington 98115-6439

NOAA - Alaska Fisheries Science Center (AFSC)

7600 Sand Point Way N.E., Seattle, Washington 98115-0070

  - Personnel

    - Chief Scientist

| Name | Gender | Nationality | Affiliation | E-mail Address |
| --- | --- | --- | --- | --- |
| Annette Dougherty | Female | USA | AFSC | Annette.Dougherty@noaa.gov |

    - Other Participating Scientists

| Name | Gender | Nationality | Affiliation | E-mail Address |
| --- | --- | --- | --- | --- |
| Steven Porter Tiffany Vance Matt Wilson | Male Female Male | USA USA USA | AFSC AFSC AFSC | Steve.Porter@noaa.gov Tiffany.C.Vance@noaa.gov Matt.Wilson@noaa.gov |

  - Administration

    - Ship Operations

Marine Operations Center, Pacific

1801 Fairview Avenue East

Seattle, Washington 98102-3767

Tel: (206) 553-4548  /  Fax: (206) 553-1109

CDR Michael Devany, NOAA

Chief, Operations Division, Pacific (MOP1)

Telephone: (206) 553-8705

Cellular: (206) 390-7527

E-mail: ChiefOps.MOP@noaa.gov

CDR Frank Wood, NOAA

Deputy Chief, Operations Division, Pacific (MOP1)

Telephone – Work: (206) 553-4764

E-mail: DeputyOps.MOP@noaa.gov

    - Scientific Operations

Dr. Phyllis J. Stabeno, PMEL		Dr. Jeffrey Napp, AFSC

Telephone: (206) 526-6453			Telephone: (206) 526-4148

E-mail: Phyllis.Stabeno@noaa.gov		E-mail: Jeff.Napp@noaa.gov

- OPERATIONS

  - Data To Be Collected

    - Scientific Computer System (SCS) - The ship's SCS shall operate throughout the cruise, acquiring and logging data from navigation, meteorological, oceanographic, and fisheries sensors.  See FOCI Standard Operating Instructions for NOAA Ship MILLER FREEMAN (SOI 5.2) for specific requirements.

  - Staging Plan – NOAA Ship MILLER FREEMAN was loaded with FOCI gear January 16, 2007, while the ship was in port in Seattle, Washington.

  - De-staging Plan - AFSC will off-load FOCI gear and samples from NOAA Ship MILLER FREEMAN while the ship is alongside Marine Operations Center, Pacific (MOP) in October. The hold will need to be opened and the loading crane will be required to remove all FOCI gear from the vessel’s hold.  The scientific party off-loading the vessel will supply vehicles from AFSC for transportation of the gear from the vessel.

  - Cruise Plan - An ichthyoplankton survey will be conducted from Unimak Pass through the Shumagin Islands and Shelikof Strait, ending at Kodiak Island.  The standard gear for this survey will be a 60-cm bongo with 0.505-mm mesh netting.  Tows will be to 100 meters or 10 meters off the bottom where water depth is shallower.  See Section 9.4.2 MF-07-08 Station Locations and Section 9.3 MF-07-08 Chartlet for a complete listing of station locations and an overview of the cruise area of operations.  Approximately 140 stations from the list will be chosen for occupation from the stations listed in Section 9.4.2 MF-07-08 Station Locations.  Live tows may be conducted with the bongos to examine larval walleye pollock condition if larvae 8-mm or less are found.  While we are working up the grid toward Kodiak Island, Alaska, we will occupy Line 8. Line 8 sampling will include 20-cm and 60-cm bongos and conductivity, temperature, and depth (CTD) profiles with Niskin bottle samples taken for chlorophyll, microzooplankton, and nutrients.  See Section 9.4.1 Line 8 Station Locations and Activities for further details.  Net tows at Line 8 are to 10 meters off the bottom.  The 60-cm bongo will be fitted with 0.505-mm and 0.333-mm mesh nets for Line 8 sampling while the 20-cm bongo mesh will be 0.153-mm.  On completion of Line 8, the 60-cm bongo will be refitted with the 0.505-mm mesh netting and cod ends and sampling will resume as before.

  - Station Locations – See  Section 9.4.2 MF-07-08 Station Locations and Section 9.4.1 Line 8 Station Locations and Activities .

  - Station Operations - The following are operations to be conducted on this cruise.  The procedures for these operations are listed in the FOCI Standard Operating Instructions for NOAA Ship MILLER FREEMAN (SOI).  Operations not addressed in the SOI and changes to standard procedures are addressed below.

- CTD/Water Sample Operations (SOI 3.2.1)

- MARMAP Bongo Tows (SOI 3.2.2)

- Bongo Larval Condition Tows (SOI 3.2.3)

- Chlorophyll Sampling Operations (SOI 3.2.11)

- SIMRAD EK-60 and 12 Khz Simrad ES-60 Scientific Echosounder Monitoring (SOI 3.2.12)

  - Underway Operations - The following are underway operations to be conducted on this cruise.  The procedures for these operations are listed in the FOCI Standard Operating Instructions for NOAA Ship MILLER FREEMAN (SOI).  Operations not addressed in the SOI and changes to standard procedures are addressed below.

- Acoustic Doppler Current Profiler (ADCP) Operations (SOI 3.2.13),

- Scientific Computer System (SCS) data acquisition (SOI 3.2.13.3),

- Fluorometer monitoring (SOI 5.3),

- Thermosalinograph monitoring (SOI 5.3).

  - Applicable Restrictions – None

  - Small Boat Operations – None

- FACILITIES

  - Equipment and Capabilities Provided by Ship

- Oceanographic winch with slip rings and 3-conductor cable terminated for CTD,

- 12 Khz hull mounted Edgetech Acoustic release transducer,

- Manual wire-angle indicator,

- Oceanographic winch with slip rings and 3-conductor cable terminated for the SBE SEACAT, for net tow operations,

- Sea-Bird Electronics’ SBE 911plus CTD system with stand, each CTD system should include underwater CTD, weights, and pinger.  There should be a deck unit for the system,

- 10-liter Niskin sampling bottles for use with rosette (10 plus 4 spares),

- Conductivity and temperature sensor package to provide dual sensors on the CTD (primary),

- AUTOSAL salinometer, for CTD field corrections,

- Sea-Bird Electronics’ SBE-19 SEACAT system for plankton tows,

- Meter block for plankton tows,

- Wire speed indicators and readout for quarterdeck, Rowe, and Marco winches,

- For meteorological observations: 2 anemometers (one R. M. Young system interfaced to the SCS), calibrated air thermometer (wet-and dry-bulb) and a calibrated barometer and/or barograph,

- Freezer space for storage of biological and chemical samples (blast and storage freezers, indicate desired temperatures),

- SIMRAD EQ-50 echosounder,

- JRC JFV-200R color sounder recorder,

- RD Instruments’ ADCP written to disk,

- Scientific Computer System (SCS),

- Minimum of 2 computers with internet and e-mail access,

- Laboratory space with exhaust hood, sink, lab tables and storage space,

- Sea-water hoses and nozzles to wash nets (quarterdeck and aft deck),

- Adequate deck lighting for night-time operations,

- Navigational equipment including GPS and radar,

- Safety harnesses for working on quarterdeck and fantail,

- Ship’s crane(s) used for loading and/or deploying.

  - Equipment and Capabilities Provided by Scientists

- Sea-Bird Electronics’ SBE 911plus CTD system,

- Sea-Bird Electronics’ SBE-19 SEACAT system,

- PMEL PC with SEASOFT software for CTD data collection and processing,

- Fluorometer, light meter and dual oxygen sensors to be mounted on CTD,

- CTD stand modified for attachment of fluorometer,

- Conductivity and temperature sensor package to provide dual sensors on the CTD (backup),

- CTD rosette sampler,

- IAPSO standard water,

- XBTs for project,

- 60-cm bongo sampling arrays,

- 20 cm bongo arrays,

- Spare wire angle indicator,

- Miscellaneous scientific sampling and processing equipment,

- Scientific ultra-cold freezer.

- Cruise Operations Database (COD)

- DISPOSITION OF DATA AND REPORTS

  - The following data products will be included in the cruise data package:

- NOAA Form 77-13d - Deck Log - Weather Observation Sheets,

- Electronic Marine Operations Abstracts,

- SCS backup,

- Calibration Sheets for all ship's instruments used,

- PMEL CTD Weather Observation Logs,

- CTD Cast Information/Rosette Log,

- Autosalinometer Logs,

- ADCP Log Sheets,

- ADCP CD (CD-RW),

- Ultra-cold Freezer Temperature Daily Log (SOI 5.4).

  - Pre- and Post-cruise Meetings - Cruise meetings may be held in accordance with FOCI Standard Operating Instructions for NOAA Ship MILLER FREEMAN (SOI 3.1.4).

- ADDITIONAL PROJECTS

  - Definition - Ancillary and piggyback projects are secondary to the objectives of the cruise and should be treated as additional investigations.  The difference between the two types of secondary projects is that an ancillary project does not have representation aboard and is accomplished by the ship's force.

  - Ancillary Projects - Any ancillary work done during this project will be accomplished with the concurrence of the Chief Scientist and on a not-to-interfere basis with the programs described in these instructions and in accordance with the NOAA Fleet Standing Ancillary Instructions.

  - Piggyback Projects – None.

- HAZARDOUS MATERIALS The field party chief shall be responsible for complying with MOCDOC 15, Fleet Environmental Compliance #07, Hazardous Material and Hazardous Waste Management Requirements of Visiting Scientists.

  - Inventory - See Section 9.2 MF-07-08 HAZMAT Inventory for a complete listing of HAZMATS brought onboard the vessel.  Spill kit contains materials for cleanup of formaldehyde, ethanol, and sodium borate.  All scientific staff onboard are trained to handle spills.

  - Material Safety Data Sheet (MSDS) - A copy of all required MSDS was delivered with the chemicals when ship was loaded.

- MISCELLANEOUS

  - Communications - Specific information on how to contact the NOAA Ship MILLER FREEMAN and all other fleet vessels can be found at:

http://www.moc.noaa.gov/phone.htm

  - Important Telephone and Facsimile Numbers and E-mail Addresses

    - Pacific Marine Environmental Laboratory (PMEL):

FOCI - Ocean Environmental Research Division (OERD2):

- (206) 526-4700 (voice)

- (206) 526-6485 (fax)

Administration:

- (206) 526-6810 (voice)

- (206) 526-6815 (fax)

    - Alaska Fisheries Science Center (AFSC):

FOCI - Resource Assessment and Conservation Engineering (RACE):

- (206) 526-4171 (voice)

- (206) 526-6723 (fax)

    - NOAA Ship MILLER FREEMAN - Telephone methods listed in order of increasing expense:

Homeport - Seattle, Washington:

- (206) 553-4589

- (206) 553-4581

- (206) 553-8344

United States Coast Guard - Kodiak, Alaska

- (907) 487-9752

- (907) 487-9753

- (907) 487-4397

- (907) 487-4398

Cellular:

- (206) 790-7594

Iridium:

- (808) 659-5684

INMARSAT Mini-M

- 011-872-761-267-346 (voice/PBX)

- 011-872-761-267-347 (voice)

- 011-872-761-267-348 (fax)

INMARSAT B

- 011-872-330-394-120 (voice)

- 011-872-330-394-121 (fax)

E-Mail: NOAA.Ship.Miller.Freeman@noaa.gov (mention the person’s name in SUBJECT field)

    - Marine Operations Center, Pacific (MOP):

Operations Division (MOP1)

- (206) 553-4548 (voice)

- (206) 553-1109 (facsimile)

- APPENDICES

  - Equipment Inventory

MF-07-08 Equipment Inventory

| Equipment | Qty | Dimension | Weight | Total Weight |
| --- | --- | --- | --- | --- |
| Larval Supply Trunk | 1 | 20”x22”x36” | 80.0 | lbs | 80.0 | lbs |
| Microzooplankton Supply Trunks | 2 | 20”x22”x36” | 90.0 | lbs | 180.0 | lbs |
| Miscellaneous Gear Trunks | 4 | 20”x22”x36” | 80.0 | lbs | 320.0 | lbs |
| 60-cm Bongo Frame | 1 | 8”x26”x60” |  |  |  |  |
| 20-cm Bongo Frame | 1 | 8”x14”x16” |  |  |  |  |
| Cases Glass Jars (32-oz) | 20 | 8”x12”x15” | 2.5 | lbs | 50.0 | lbs |
| Cases Glass Jars (8-oz) | 6 | 4”x6”x8” | 1.3 | lbs | 7.8 | lbs |
| 20-L Container, Formaldehyde 37% | 3 |  | 40.0 | lbs | 120.0 | lbs |
| 20-L Container, Ethanol 95% | 1 |  | 40.0 | lbs | 40.0 | lbs |
| 20-L Container, Sodium Borate Solution, Saturated | 1 |  | 40.0 | lbs | 40.0 | lbs |
| 500-g Container, Sodium Borate | 2 |  | 1.0 | lbs | 2.0 | lbs |
| 1 L Containers Absolute Alcohol | 4 |  | 1.5 | lbs | 1.5 | lbs |
| Spill Kit | 1 | 8”x12”x14” | 1.5 | lbs | 1.5 | lbs |
| TOTAL WEIGHT: | 842.8 | lbs |

  - HAZMAT Inventory

MF-07-08 HAZMAT Inventory

| Chemical | CAS Number | Respondee | Org | Qty | H | F | R | Storage Color Code | Hazard Class | Packing Group Number | UN | Reportable Quantity | Response Indices |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Ethanol, 95% | 64-17-5 | Dougherty | AFSC | 20-L | 3 | 4 | 2 | Flammable | 3 | II | 1170 | 5,000 LBS | 1 |
| Formaldehyde, 37% | 50-00-0 | Dougherty | AFSC | 60-L | 3 | 2 | 2 | Flammable | 3 & 8 | III | 1198 | 100 LBS | 1 |
| Sodium Borate | 1330-43-4 | Dougherty | AFSC | 1-kg | 1 | 0 | 0 | General | Not regulated |  |  |  | 2 |
| Sodium Borate Solution, Saturated | mix | Dougherty | AFSC | 20-L | 1 | 0 | 0 | General | Not regulated |  |  |  | 2 |
| Absolute Alcohol | mix | Dougherty | AFSC | 4-L | 3 | 4 | 2 | General | 3 |  | 1170 |  |  |
| Spill Response 1: Ventilate area of leak or spill. Remove all sources of ignition. Wear appropriate personal protective equipment. Isolate hazard area. Keep unnecessary and unprotected personnel from entering. Contain and recover liquid when possible. Use non-sparking tools and equipment. Collect liquid in an appropriate container or absorb with an inert material (e. g., vermiculite, dry sand, or earth), and place in a chemical waste container. Do not use combustible materials, such as saw dust. Do not flush to sewer! If a leak or spill has not ignited, use water spray to disperse the vapors, to protect personnel attempting to stop leak, and to flush spills away from exposures. U.S. Regulations (CERCLA) requires reporting spills and releases to soil, water and air in excess of reportable quantities. The toll free number for the U.S. Coast Guard National Response Center is (800) 424-8802. |
| Spill Response 2: Ventilate area of leak or spill. Wear appropriate personal protective equipment. Pick up and place in a suitable container for reclamation or disposal, using a method that does not generate dust. |

  - MF-07-08 Station Locations

  - Tables

    - MF-07-08 Line 8 Station Locations and Activities

| Station | Latitude | Longitude | Lat (dd) | Lon (dd) | CTDB | Chlor | Nuts | MZ | 20/60 Bongo |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FOX61 | 57° | 43.20' | N | 155° | 15.60' | W | 57.72 | -155.26 | x | x | x | x | x |
| FOX60 | 57° | 40.80' | N | 155° | 10.20' | W | 57.68 | -155.17 | x | x | x | x | x |
| FOX59 | 57° | 38.40' | N | 155° | 04.20' | W | 57.64 | -155.07 | x | x | x | x | x |
| FOX58 | 57° | 36.60' | N | 155° | 00.60' | W | 57.61 | -155.01 | x | x | x | x | x |
| FOX57 | 57° | 33.00' | N | 154° | 52.80' | W | 57.55 | -154.88 | x | x | x | x | x |
| FOX56 | 57° | 31.20' | N | 154° | 46.80' | W | 57.52 | -154.78 | x | x | x | x | x |
| FOX55 | 57° | 28.80' | N | 154° | 42.00' | W | 57.48 | -154.70 | x | x | x | x | x |

    - MF-07-08 Station Locations

| Potential Station # | xy grid | Lat Deg | Lat DecMin |  | Long Deg | Long DecMin |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | gf107 | 54° | 24.5310 | N | 164° | 4.2900 | W |
| 2 | gh107 | 54° | 17.6436 | N | 163° | 49.6620 | W |
| 3 | gh109 | 54° | 24.9012 | N | 163° | 37.8420 | W |
| 4 | gf109 | 54° | 31.7880 | N | 163° | 52.4400 | W |
| 5 | gh111 | 54° | 32.1588 | N | 163° | 25.9920 | W |
| 6 | gp123 | 54° | 48.15 | N | 161° | 17.19 | W |
| 7 | gp125 | 54° | 55.4118 | N | 161° | 5.2260 | W |
| 8 | gr125 | 54° | 48.5250 | N | 160° | 51.1440 | W |
| 9 | gt125 | 54° | 41.6382 | N | 160° | 37.1100 | W |
| 10 | gv125 | 54° | 34.7508 | N | 160° | 23.1240 | W |
| 11 | gv127 | 54° | 42.0084 | N | 160° | 11.2200 | W |
| 12 | gt127 | 54° | 48.8952 | N | 160° | 25.1760 | W |
| 13 | gr127 | 54° | 55.7826 | N | 160° | 39.1740 | W |
| 14 | gp127 | 55° | 2.6694 | N | 160° | 53.2200 | W |
| 15 | gn127 | 55° | 9.5568 | N | 161° | 7.3140 | W |
| 16 | gl127 | 55° | 16.4436 | N | 161° | 21.4560 | W |
| 17 | B4 | 55° | 21.7800 | N | 161° | 38.3400 | W |
| 18 | B2 | 55° | 20.7000 | N | 161° | 2.1600 | W |
| 19 | go133 | 55° | 30.0000 | N | 160° | 20.0000 | W |
| 20 | gp135 | 55° | 31.6992 | N | 160° | 4.8480 | W |
| 21 | gp137 | 55° | 38.9562 | N | 159° | 52.6620 | W |
| 22 | gr135 | 55° | 24.8118 | N | 159° | 50.9400 | W |
| 23 | gt135 | 55° | 17.9250 | N | 159° | 37.0800 | W |
| 24 | gx135 | 55° | 4.1508 | N | 159° | 9.4860 | W |
| 25 | gz135 | 54° | 57.2640 | N | 158° | 55.7580 | W |
| 26 | hb135 | 54° | 50.3766 | N | 158° | 42.0720 | W |
| 27 | gz139 | 55° | 11.7786 | N | 158° | 31.6980 | W |
| 28 | gx139 | 55° | 18.6654 | N | 158° | 45.3600 | W |
| 29 | gv139 | 55° | 25.5528 | N | 158° | 59.0640 | W |
| 30 | gt139 | 55° | 32.4396 | N | 159° | 12.8100 | W |
| 31 | gv143 | 55° | 40.0674 | N | 158° | 34.7160 | W |
| 32 | gx143 | 55° | 33.1806 | N | 158° | 21.0780 | W |
| 33 | gz143 | 55° | 26.2932 | N | 158° | 7.4940 | W |
| 34 | hb143 | 55° | 19.4064 | N | 157° | 53.9460 | W |
| 35 | hb141 | 55° | 12.1488 | N | 158° | 6.0360 | W |
| 36 | hd143 | 55° | 12.5190 | N | 157° | 40.4400 | W |
| 37 | hf147 | 55° | 20.1468 | N | 157° | 2.8380 | W |
| 38 | hd147 | 55° | 27.0342 | N | 157° | 16.2300 | W |
| 39 | hb147 | 55° | 33.9210 | N | 157° | 29.6640 | W |
| 40 | gz147 | 55° | 40.8078 | N | 157° | 43.1340 | W |
| 41 | gx147 | 55° | 47.6952 | N | 157° | 56.6520 | W |
| 42 | gv147 | 55° | 54.5820 | N | 158° | 10.2120 | W |
| 43 | gr151 | 56° | 22.8708 | N | 158° | 12.6660 | W |
| 44 | gt151 | 56° | 15.9840 | N | 157° | 59.0940 | W |
| 45 | gv151 | 56° | 9.0972 | N | 157° | 45.5640 | W |
| 46 | gx151 | 56° | 2.2098 | N | 157° | 32.0760 | W |
| 47 | gz151 | 55° | 55.3230 | N | 157° | 18.6300 | W |
| 48 | hb151 | 55° | 48.4356 | N | 157° | 5.2260 | W |
| 49 | hd151 | 55° | 41.5488 | N | 156° | 51.8640 | W |
| 50 | hf151 | 55° | 34.6614 | N | 156° | 38.5440 | W |
| 51 | hh151 | 55° | 27.7746 | N | 156° | 25.2660 | W |
| 52 | hh153 | 55° | 35.0322 | N | 156° | 13.0980 | W |
| 53 | hf153 | 55° | 41.9190 | N | 156° | 26.3400 | W |
| 54 | hd153 | 55° | 48.8058 | N | 156° | 39.6300 | W |
| 55 | hb153 | 55° | 55.6932 | N | 156° | 52.9560 | W |
| 56 | gz153 | 56° | 2.5800 | N | 157° | 6.3180 | W |
| 57 | gx153 | 56° | 9.4674 | N | 157° | 19.7280 | W |
| 58 | gv153 | 56° | 16.3542 | N | 157° | 33.1800 | W |
| 59 | gt153 | 56° | 23.2416 | N | 157° | 46.6740 | W |
| 60 | gt155 | 56° | 30.4986 | N | 157° | 34.2120 | W |
| 61 | gv155 | 56° | 23.6118 | N | 157° | 20.7540 | W |
| 62 | gx155 | 56° | 16.7244 | N | 157° | 7.3440 | W |
| 63 | gz155 | 56° | 9.8376 | N | 156° | 53.9700 | W |
| 64 | hd155 | 55° | 56.0634 | N | 156° | 27.3540 | W |
| 65 | hf155 | 55° | 49.1766 | N | 156° | 14.1000 | W |
| 66 | hh155 | 55° | 42.2892 | N | 156° | 0.8940 | W |
| 67 | hf157 | 55° | 56.4336 | N | 156° | 1.8240 | W |
| 68 | hd157 | 56° | 3.3210 | N | 156° | 15.0360 | W |
| 69 | hb157 | 56° | 10.2078 | N | 156° | 28.2900 | W |
| 70 | gz157 | 56° | 17.0952 | N | 156° | 41.5800 | W |
| 71 | gx157 | 56° | 23.9820 | N | 156° | 54.9180 | W |
| 72 | gu158 | 56° | 40.0000 | N | 157° | 13.0000 | W |
| 73 | gv159 | 56° | 38.1264 | N | 156° | 55.7880 | W |
| 74 | gx159 | 56° | 31.2396 | N | 156° | 42.4500 | W |
| 75 | gz159 | 56° | 24.3522 | N | 156° | 29.1540 | W |
| 76 | hb159 | 56° | 17.4654 | N | 156° | 15.9000 | W |
| 77 | hd159 | 56° | 10.5780 | N | 156° | 2.6820 | W |
| 78 | hf159 | 56° | 3.6912 | N | 155° | 49.5060 | W |
| 79 | hd161 | 56° | 17.8356 | N | 155° | 50.2920 | W |
| 80 | hb161 | 56° | 24.7224 | N | 156° | 3.4680 | W |
| 81 | gz161 | 56° | 31.6098 | N | 156° | 16.6860 | W |
| 82 | gx161 | 56° | 38.4966 | N | 156° | 29.9460 | W |
| 83 | gv161 | 56° | 45.3840 | N | 156° | 43.2480 | W |
| 84 | gt163 | 56° | 51.0000 | N | 156° | 45.0000 | W |
| 85 | gv163 | 56° | 52.6410 | N | 156° | 30.6660 | W |
| 86 | gx163 | 56° | 45.7542 | N | 156° | 17.4000 | W |
| 87 | gz163 | 56° | 38.8674 | N | 156° | 4.1820 | W |
| 88 | hb163 | 56° | 31.9800 | N | 155° | 51.0000 | W |
| 89 | hd163 | 56° | 25.0932 | N | 155° | 37.8600 | W |
| 90 | hd165 | 56° | 32.3502 | N | 155° | 25.3860 | W |
| 91 | hb165 | 56° | 39.2376 | N | 155° | 38.4900 | W |
| 92 | gz165 | 56° | 46.1244 | N | 155° | 51.6360 | W |
| 93 | gx165 | 56° | 53.0118 | N | 156° | 4.8180 | W |
| 94 | gv165 | 56° | 59.8986 | N | 156° | 18.0420 | W |
| 95 | gv167 | 57° | 7.1562 | N | 156° | 5.3760 | W |
| 96 | gx167 | 57° | 0.2688 | N | 155° | 52.1880 | W |
| 97 | gz167 | 56° | 53.3820 | N | 155° | 39.0480 | W |
| 98 | hb167 | 56° | 46.4946 | N | 155° | 25.9440 | W |
| 99 | hd167 | 56° | 39.6078 | N | 155° | 12.8760 | W |
| 100 | hd169 | 56° | 46.8654 | N | 155° | 0.3240 | W |
| 101 | hb169 | 56° | 53.7522 | N | 155° | 13.3500 | W |
| 102 | gz169 | 57° | 0.6390 | N | 155° | 26.4180 | W |
| 103 | gx169 | 57° | 7.5264 | N | 155° | 39.5220 | W |
| 104 | gv169 | 57° | 14.4132 | N | 155° | 52.6680 | W |
| 105 | gt169 | 57° | 21.3000 | N | 156° | 5.0000 | W |
| 106 | gt171 | 57° | 27.0000 | N | 155° | 46.0000 | W |
| 107 | gv171 | 57° | 21.6708 | N | 155° | 39.9180 | W |
| 108 | gx171 | 57° | 14.7840 | N | 155° | 26.8140 | W |
| 109 | gz171 | 57° | 7.8966 | N | 155° | 13.7460 | W |
| 110 | hb171 | 57° | 1.0098 | N | 155° | 0.7200 | W |
| 111 | hd171 | 56° | 54.1224 | N | 154° | 47.7360 | W |
| 112 | hb173 | 57° | 8.2668 | N | 154° | 48.0480 | W |
| 113 | gz173 | 57° | 15.1542 | N | 155° | 1.0380 | W |
| 114 | gx173 | 57° | 22.0410 | N | 155° | 14.0640 | W |
| 115 | gv173 | 57° | 28.9284 | N | 155° | 27.1260 | W |
| 116 | gt173 | 57° | 37.0000 | N | 155° | 28.0000 | W |
| 117 | gv175 | 57° | 36.1854 | N | 155° | 14.2980 | W |
| 118 | gx175 | 57° | 29.30 | N | 155° | 1.27 | W |
| 119 | gz175 | 57° | 22.4112 | N | 154° | 48.2820 | W |
| 120 | FOX56 | 57° | 31.2000 | N | 154° | 46.8000 | W |
| 121 | FOX57 | 57° | 33.0000 | N | 154° | 52.8000 | W |
| 122 | FOX58 | 57° | 36.6000 | N | 155° | 0.6000 | W |
| 123 | FOX59 | 57° | 38.4000 | N | 155° | 4.2000 | W |
| 124 | FOX60 | 57° | 40.8000 | N | 155° | 10.2000 | W |
| 125 | FOX61 | 57° | 43.2000 | N | 155° | 15.6000 | W |
| 126 | gx177 | 57° | 36.5556 | N | 154° | 48.4380 | W |
| 127 | gv177 | 57° | 43.4430 | N | 155° | 1.4220 | W |
| 128 | gv179 | 57° | 50.7006 | N | 154° | 48.4980 | W |
| 129 | gx179 | 57° | 43.8132 | N | 154° | 35.5620 | W |
| 130 | gx181 | 57° | 51.0708 | N | 154° | 22.6380 | W |
| 131 | gz181 | 57° | 44.1834 | N | 154° | 9.7740 | W |
| 132 | gz183 | 57° | 51.4410 | N | 153° | 56.8500 | W |
| 133 | gx183 | 57° | 58.3278 | N | 154° | 9.6720 | W |
| 134 | gx185 | 58° | 5.5854 | N | 153° | 56.6640 | W |
| 135 | gz185 | 57° | 58.6986 | N | 153° | 43.8840 | W |
| 136 | gz189 | 58° | 13.2132 | N | 153° | 17.8200 | W |
| 137 | gx189 | 58° | 20.1000 | N | 153° | 30.5160 | W |
| 138 | gv189 | 58° | 26.9874 | N | 153° | 43.2480 | W |
| 139 | gv193 | 58° | 41.5020 | N | 153° | 16.8300 | W |
| 140 | gx193 | 58° | 34.6152 | N | 153° | 4.1820 | W |
| 141 | gz193 | 58° | 27.7278 | N | 152° | 51.5760 | W |
| 142 | gz197 | 58° | 42.2424 | N | 152° | 25.1460 | W |
| 143 | gx197 | 58° | 49.1298 | N | 152° | 37.6740 | W |
| 144 | gv197 | 58° | 56.0166 | N | 152° | 50.2320 | W |
| 145 | gt197 | 59° | 2.9040 | N | 153° | 2.8260 | W |
| 146 | gt201 | 59° | 17.42 | N | 152° | 35.95 | W |
| 147 | gv201 | 59° | 10.5318 | N | 152° | 23.4480 | W |
| 148 | gx201 | 59° | 3.6444 | N | 152° | 10.9740 | W |
| 149 | gz203 | 59° | 4.01 | N | 151° | 45.16 | W |
| 150 | hb203 | 58° | 57.1278 | N | 151° | 32.8080 | W |
| 151 | hb201 | 58° | 49.8702 | N | 151° | 46.1340 | W |
| 152 | hb199 | 58° | 42.6132 | N | 151° | 59.4180 | W |
| 153 | hd197 | 58° | 28.4688 | N | 152° | 0.2040 | W |
| 154 | hd199 | 58° | 35.7258 | N | 151° | 47.0100 | W |
| 155 | hd201 | 58° | 42.9834 | N | 151° | 33.7740 | W |
| 156 | hd203 | 58° | 50.2410 | N | 151° | 20.4840 | W |
| 157 | hf203 | 58° | 43.35 | N | 151° | 8.20 | W |
| 158 | hh207 | 58° | 50.98 | N | 150° | 29.40 | W |
| 159 | hh205 | 58° | 43.72 | N | 150° | 42.69 | W |
| 160 | hh203 | 58° | 36.47 | N | 150° | 55.94 | W |
| 161 | hh201 | 58° | 29.21 | N | 151° | 9.14 | W |
| 162 | hf201 | 58° | 36.10 | N | 151° | 21.44 | W |
| 163 | hf199 | 58° | 28.8390 | N | 151° | 34.6320 | W |
| 164 | hh199 | 58° | 21.9516 | N | 151° | 22.2900 | W |
| 165 | hh197 | 58° | 14.69 | N | 151° | 35.40 | W |
| 166 | hf197 | 58° | 21.5814 | N | 151° | 47.7840 | W |
| 167 | hh195 | 58° | 7.44 | N | 151° | 48.46 | W |
| 168 | hh193 | 58° | 0.18 | N | 152° | 1.48 | W |

9.5  Deemed Exports-NAO 207-12

The procedures for foreign nationals are listed in the FOCI Standard Operating Instructions for NOAA Ship MILLER FREEMAN (SOI), Section 9.0